## Slide 1: Airline Planning and Operations Airline networks
Danica Babić
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Network development/design
2

## Slide 3: Airline Network Planning
An airline network’s choice of structure defines the core product and determines:
  Cost structure and
  Revenue potential.
The goal is to create an effective network strategy that optimizes revenue and makes the most efﬁcient use of expensive aircraft assets.
Network design main questions:
  Which markets to serve?
  How to serve the markets – route choice?

## Slide 4: Network Planning: Markets
Origin and destination (city-pair) markets:
Point-to-point markets:
  Two hubs (e.g. London and Frankfurt);
  A hub and a secondary or tertiary airport (e.g. Frankfurt and Belgrade);
  Two secondary or tertiary airports (e.g. Belgrade and Bari).
One-hub market:
  From a secondary or tertiary airport to another secondary or tertiary airport via a hub (e.g. Reykjavik -Frankfurt-Poznan);
  From a secondary or tertiary airport to a hub via another hub (e.g. Graz-Amsterdam-New York);
  From a hub to a secondary or tertiary airport via another hub ( e.g. Washington-London-Edinburgh)
Double-hub network usually involves originating from a secondary or tertiary airport, transfers at two hubs and resulting in the final destination at another secondary or tertiary airport (e.g. Graz-Amsterdam-Detroit-Milwaukee).

## Slide 5: Airline Network Planning: Routes
A route links two points using the same aircraft under the same flight number:
  A non-stop service – there is one flight-leg between the start and end-point (e.g. London-Edinburgh)
  A direct service – there are two or more flight legs because one or more stops are made (e.g. Belgrade-Larnaca-Dubai)
If the same flight number is used but a change of aircraft is required at an intermediate point, this presents two connecting routes (online, code-share or interline connection)
Route evaluation process:
  forecast of the potential demand (and expected revenues),
  Origin & Destination demand and transfer demand,
  airline market share

## Slide 6
Network planning
Long term
Strategy
Short term
Tactics
Fleet planning
Flight schedule design:
Frequency
Departure time
Fleet assignment
Aircraft rotations
Crew planning
Price definition
Revenue management
Slot management
Ticket sales and distribution
Operations centre
Airline planning process…
Time frame
Type the decision

## Slide 7: Airline Network Structures
Most common network structures among airlines:
  Point-to-point
  Hub-and-spoke

## Slide 8: Point-to-Point (PP) Network
Line network structure
Grid network structure
Fully connected network structure

## Slide 9: Point-to-Point Network
Point-to-point network structures connect each airport in the network with direct flights without intermediate stops.
Conditions that favor a point-to-point network :
  The distance between the airports is relatively small
  Demand between the airports is high
  The total number of airports in the network is small

## Slide 10: Point-to-Point Network - Benefits
Greater reliability of flight schedule:
  Direct flights do not depend on other flights in the flight schedule,
  the possibility of a “domino effect” is reduced – the case in which one flight delay causes a delay of subsequent flights in the schedule and an increase in that delay during the day.
Greater utilization of aircraft in the fleet:
  Flights in the flight schedule are not connected, which leaves the freedom to plan flights during the day that maximize the utilization of each individual aircraft.

## Slide 11: Point-to-point network - shortcomings
The frequency on each route during the day is relatively small.
A large number of routes necessary to achieve greater network connectivity:
  If there are n airports in the network, it is necessary
  routes
  to connect all airports!

## Slide 12: Hub-and-Spoke (HS) Network
HS networks consists of a hub, which is a central airport, and a number of city airport pairs (spokes) that extend radially relative to it
Conditions that favor HS network:
  Demand between the two airports is comparatively low
  The total number of airports served by the airline is large
I
C
D
A
G
E
F
B
H

## Slide 13: Hub Connectivity
The number of potential connections at the hub grows exponentially with the increase in the number of markets served from a given hub.
When airports are connected via hubs, the number of available city-pairs is then higher in comparison to being connected directly.
Example: Replacing point to point routes by introducing a central hub will increase possible routes 11 times over, maximizing the number of marketable connections.
A
B
C
D
E
F
I
J
G
H
A
B
C
D
E
F
I
J
G
H
Hub
a) 5 routes b) 55 routes c) 190 routes

## Slide 14: Hub Connectivity
Each market served in HS network is connected to a hub
This requires a smaller number of flights, as opposed to the number of flights that would be required to cover all markets in the case of a point-to-point network.
If the network has n nodes, the number of connections is:
I
C
D
A
G
E
F
B
Hub

## Slide 15: Hub and Spoke Network - Benefits
Higher frequencies per day on each route :
  By directing passengers to the hub, the airline achieves a significantly higher traffic density and this allows offering a higher frequency.
The number of available city pairs is higher in comparison to point-to-point network
Fewer aircraft needed to serve the network

## Slide 16: Hub and Spoke Network - Disadvantages
Reliability in the flight schedule and integrity of the operation is low due to delays and congestion at the hub.
Passengers travel longer distances to their final destinations (by additional flights to the hub in relation to a direct route).
Due to stopping in the hub, the average stage-length decreases.
Establishing a hub can be very expensive as a result of complex operations and capital costs.
Reduced aircraft utilization :
  Aircraft may spend a significant amount of time on the ground during turn arounds, operating waves of flights that provide a suitable connecting timetable to allow all passengers to make their transfers. This can result in peak periods of activity resulting in slot delays.

## Slide 17: Hub Types (1)
H
H
H
H
H
Directional or hourglass hub
Multi-directional hourglass hub
Hinterland hub
Regional hub
Wayport

## Slide 18: Typical Hub-and-Spoke Structures
H
H1
H2
H1
H2

## Slide 19: Spatial Configuration of Network Structure - Analysis
Graph theory – used for basic analysis of spatial configuration of networks and analysis of the effect of merging two airlines.
Hub location - aims to spatially optimize the hub-and-spoke network.
  Nodes in the network are divided into nodes and hubs.
  Hubs are a special type of node positioned in such a way to allow connections between other nodes in the network - transfer nodes.
  Other nodes in the network are the source or destination.

## Slide 20: Spatial Configuration of Network Structure - Analysis
Measurement of concentration and dispersion - to assess the market concentration of the airline or to analyze the relationship between the price of transportation and the concentration of power of the airline for the purpose of assessing the monopoly position.
  Different concentration measures can be used to measure the level of spatial concentration of the network, such as the coefficient of variance, the Herfindahl index, the Teil measure of entropy, as well as the Gini index.

## Slide 21: Temporal Configuration of A Network Structure
Temporal configuration - measuring the time concentration of flights at a particular airport.
Temporal concentration of a network can be defined as the coordination of flight schedules at a particular airport resulting in an appropriate number and the quality of indirect connections offered through a given hub.
The number and quality of indirect connections can be improved on the basis of a well-designed flight schedule or by adopting a wave system in the airline's flight schedule.

## Slide 22: Space-Time Continuum
An airline network is a set of connected airports in space and time.
The development of the airline network must be observed through the development of both dimensions: space and time.
The structure of the airline's network is defined as the level of spatial and temporal concentration of traffic flows in a given network.

## Slide 23: Space-Time Continuum
Spatial and temporal concentration - the four most common structures of an airline's network
In addition to the structures shown, airline networks vary in a two-dimensional continuum of spatial and temporal concentration.
Level of spatial concentration | The level of time concentration in the hub | 
 | Co-ordinated | Random
Concentrated | Hub-and-spoke | Random-radial
Deconcentrated | Co-ordinated /Deconcentrated | Point-to-point

## Slide 24: Temporal Concentration
What is the temporal concentration of airline networks?
  Organization of flights in the flight schedule which results in a certain number and quality of indirect connections at the airline's hub.
The number and quality of indirect connections can be improved on the basis of a well-designed flight schedule or the adoption of a wave system in the flight schedule of airlines.
The structure of the wave system consists of the number of waves, their time schedule and the structure of individual waves.

## Slide 25: Temporal Organization of Flights
At the hub, flights are organized so that the first wave of flights arrive at a similar time, passengers have enough time to transfer to a next flight (Minimum Connect Time MCT), followed by a concentration of departing flights.
Minimum
Connecting time
Arrival wave
Departure wave
Time

## Slide 26: Temporal Organization of Flights
Two consecutive waves, consisting of the arrival wave and then subsequent departure wave , form a wave system or connection complex.
Each wave system is determined by a time frame - the period from the moment of the first landing in the hub of the incoming wave to the moment of the last takeoff from the outgoing wave.
  The wider this time frame, the greater the number of available connections and vice versa.
The arrival/departure wave is determined by the amplitude - the maximum number of flights in the wave at a given time.
  The amplitude is defined by the capacity that the airline has at the hub

## Slide 27: Reasons for the Formation of a Wave System
Allows passengers to continue their journey from any of the incoming flights to any of the outgoing flights while spending a minimum of time waiting at the transfer airport;
  This is especially relevant in Europe, where only a small number of routes have high-frequency services.
An airline can become efficient in providing transfer traffic for its flights.

## Slide 28: Key Elements of Hub Development
Geographical location
Local and transfer traffic
Dominance in the hub
Capacity expansion possibilities
Mid-haul/Long-haul routes (Air France)
Long-haul/Long-haul routes (Emirates)
Airport equipment
Timetable coordination
Attractiveness from the passenger aspect
Hub efficiency

## Slide 29: Advantage of Geographical Location
The significance of “sixth freedom” of the air
KLM, SAS, Austrian Airlines, TAP...
Emirates, Qatar, Etihad, Gulf Air...
Cathay Pacific, Singapore Airlines, Thai....
Singapore
Vienna
Frankfurt
Zurich
Amsterdam
Paris
London
Copenhagen
Brisbane
Auckland
Sydney
Christchurch
Melbourne
Adelaide

## Slide 30: Network structure and route evaluation

## Slide 31: Route Planning Models
Route planning requires a detailed approach to route evaluation and includes the following:
  Traffic forecast, yield forecasts, operating costs estimation and estimated aircraft productivity for a specific route, for several years in the future;
  Estimation of market share and total route demand based on passenger choice models involving multiple airlines and different flight schedules.
The outcome depends on the number of competitors within the market and their response to new service.

## Slide 32: Route Planning Models
Decisions made about new routes are based on profit opportunities but have a direct impact on fleet and flight schedule planning, so it is necessary to have:
  All valid data to calculate the profitability of the route for the defined time frame.
Airlines usually analyse route profitability on a monthly basis.
Point-to-point network: route profitability is calculated independently of other routes in the network.
Hub-and-spoke network: the route is seen as an element of a larger system, as the full journey through which the passenger travels usually includes several flights stages.

## Slide 33: Route Planning and Evaluation
Economic aspects in route planning and evaluation:
  Forecast of potential passenger/goods demand (as well as expected revenues) for the planned route (RPK, RTK….);
  Planning average load factor (%)
  ASK need to be generated to meet the traffic demand
  In the hub-and-spoke network, arrival/departure flights (connections) can support the new route and impact its profitability;
  The airline's market share for total forecast demand for the new route depends on current and expected future competition;

## Slide 34: Route Evaluation - Other Aspects
Other important aspects to consider:
  Technical performance ability for providing the service on the planned route depends on the available aircraft in the fleet (adequate range and appropriate capacity);
  Operating costs of the available aircraft in the fleet;
  If the new route includes a new destination, it must be taken into account that there will be additional set up and infrastructure costs due to hiring of labor, opening an office, airport services...
  Legal regulations, limited capacity at the airport (slots) can further increase costs so that the route becomes unprofitable.

## Slide 35: Route Profitability Methodology
The idea of route profitability analysis is to allocate all revenues and costs to the appropriate flights.
Revenue usually includes :
  Revenue from ticket sales for the flight;
  Other ancillary revenues on a specific flight, e.g. collection of excess luggage, sale of products during the flight, fuel and security fees, income from the transport of cargo in the trunk, etc.

## Slide 36: Route Profitability Measurement
The airline's revenue depends on the demand in each O&D market:
  Prices are determined on the basis of competition or determined due to regulation.
  Revenues are generated on the basis of travel itineraries.
Decisions about the final flight schedule are often made at the route level or individual flight:
  Airline managers make decisions about which flights to remove so that other flights can be added.

## Slide 37: Route Profitability Measurement
The costs for an airline depends on the flight schedule and the structure of the fleet:
  Fleet affects fixed costs (capital costs) and variable costs (fuel combustion, maintenance, etc.);
  The flight schedule affects resource utilization and thus affects variable costs;
  Costs are measured based upon the actual route and at the network level.

## Slide 38: Route Profitability Analysis Methodology
Flight operating costs are usually divided into:
  Direct operating costs:
    Variable costs related to passengers;
    Variable flight costs;
    Fixed costs related to capacity.
  Indirect operating costs :
    Passenger service at the airport;
    Sales and marketing costs;
    Administrative costs.

## Slide 39: Route Profitability Analysis Methodology
Some revenue and cost can’t be attributed to a specific flight, such revenues and expenses should be allocated to flights by applying a rule based on how they are generated:
    Number of flight hours;
    Number of block hours;
    Available seat kilometers – ASK;
    Revenue passenger kilometers – RPK;
    Average stage-length.....

## Slide 40: Approaches to Flight Profitability Measurement
The first step is to add/change/remove the flight in question and then measure the profitability for the rest of the network.
This approach is desirable because it allows measuring the effect on the entire network, both through the impact on costs and through the impact on revenue.
Allocate all costs and revenues to individual flights and then treat each flight as independent of the rest of the network.
This approach does not cover the effects of the entire network, which is very important in the hub-and-spoke case.

## Slide 41: Literature
Burghouwt G. Airline Network Development in Europe and its Implications for Airport Planning Ashgate: Aldershot, 2007.
Dennis N. Airline hub operations in Europe. Journal of Transport Geography 1994; 2(4): 219– 233.
Holloway, S., 2003. Straight and Level: Practical Airline Economics, Ashgate Publishing Limited. Gower House, Croft Road, Aldershot, Hampshire GU11 3HR, England.
Alderighi, M., Cento, A., Nijkamp, P. and Rietveld, P. 2007. Assessment of New Hub‐and‐Spoke and Point‐to‐Point Airline Network Configurations, Transport Reviews, 27:5, pp. 529-549.

## Slide 42
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com