## Slide 1: Airline Planning and Operations Fleet planning
Slavica Dožić
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Planning in Air Transportation
Airport planning
Fleet planning
Route network planning
Airways network planning
Flight schedule planning

## Slide 3: Planning in air transportation
Planning in air transportation includes airport planning, fleet planning, route network planning, flight schedules planning and airways network planning
Airport planning and airways network planning refer to the planning of infrastructure
Fleet planning, route network planning, and flight schedules planning refer to airline planning
The Air Transportation system is very complex and multi-layered involving many components and high capital/operating costs.

## Slide 4: Airline planning process
One of the main factors that affects airline success is matching supply and demand within the economic market that it operates.
  Airlines should aim to be profitable, while keeping customers (passengers) satisfied, keeping costs to a minimum.
To make an adequate passenger demand forecast, past trends should be analysed, as well as the corresponding influencing factors.

## Slide 5: Airline planning process
An adequate forecast for the airline means a high probability of success for the business
Based on the air passenger demand forecast, decisions need to be made relating to:
  Route network design and development
  Determining optimum flight frequencies
  Structure and design of the flight schedules
  Determination of the fleet size and development
  pricing policy

## Slide 6: Airline planning process
Determining passenger demand should be the first step for airline planning and fleet development
Based on current and past data, future air passenger demand should be determined
Once demand has been determined the route network should be designed with appropriate flight frequencies followed by the airline fleet and resource planning process.

## Slide 7: Airline planning process
Air travel demand analisys and forecast
Network planning
Frequencies determination
Fleet planning

## Slide 8: Fleet Planning
It is important to determine the capacity available to match the demand for the airline
Fleet planning in an airline is very similar to other planning activities
  It involves great complexity and great uncertainty
To ensure efficiencies and optimisation:
  Involve in the process engineers, as well as the experts from the other areas (economy, management, law, etc.)
  Iterative process from all stakeholders to reach solutions
Decision makers and planners must be able project into the future and factor in many variables, uncertainties, and unpredictable events.

## Slide 9: Fleet Planning – Definition
From the airline perspective, fleet planning is the process by which an airline acquires and manages appropriate aircraft capacity in order to serve anticipated markets over a variety of defined periods of time with a view to maximising corporate wealth.
          (Clark, 2007)

## Slide 10: Expansion of Fleet Planning
Fleet planning is a permanent process, rather than just making a one off decision
  Fleet planning is an iterative process that requires constant evaluation and feedback to improve the product offering and drive efficiencies for the airline
Aircraft acquisition – buying or leasing
  The decision related to buying or leasing is made based on factors such as finance, aircraft availability, airline needs, etc.

## Slide 11: Fleet Planning – Definition
Fleet management implies the use of the aircraft in an appropriate manner, but also includes making decision to replace aircraft, to sell aircraft, to change the aircraft purpose or to lease aircraft to another airline or aircraft operator
The capacity of an aircraft describes its size and ability to serve the demand:
  Aircraft size and frequency are key factors when solving the capacity constrains faced by network planners

## Slide 12: Fleet Planning – Definition
Anticipated markets imply certain changes in the current market
  Airlines need to be flexible to respond to market fluctuations in order to meet the needs of passenger demand
Specific Aircraft should be utilized depending upon their operational life span
  The fleet should be in accordance with the short-term and long-term plans
  In the short-term, one type of aircraft can meet the needs of an airline
  In the long run, such a decision may be unacceptable

## Slide 13: Fleet Planning
Large capital investments are necessary for aircraft acquisition  all aspects need to be considered and decisions should be made to enable long-term utilization of aircraft
The needs of the airline should be harmonized with its capabilities, i.e. with the funds available for investments, i.e. with profitability
Airline profitability influences the decisions regarding fleet acquisition, but also fleet efficiency can impact the profitability

## Slide 14: Fleet Planning
Determination of appropriate capacity for the given demand and market conditions
Fleet development
  Airline policy
  Route network/network structure
  Market

## Slide 15: Fleet Planning
From fleet planning definition 
  Fleet planning process + decision making + significant investment
It is important to understand
  Who the decision makers are
  Who manages the fleet

## Slide 16: The Management and Decision Process
Pilots
Engineers
Marketing experts
Finance experts

## Slide 17: Pilots
  It is important to note that pilots have traditionally been involved in the decision making processes carried out by the airlines.
  They were asked about aircraft acquisition
  How they manage the aircraft

## Slide 18: Engineers
A vitally important part of the process was input from the airlines engineers, representing the majority of the staff in the airline’s planning departments
While making decisions related to fleet planning, engineers
  Evaluate the available aircraft
  Research aircraft take-off and en-route performance
  Check compatibility with airports to be flown
  Check the system reliability, as well as maintenance requirements
This approach led to a optimum and technically justified decision

## Slide 19: Expertise from Marketing and Finance
Deregulation  market changes in the airline industry  airlines started to work in accordance with air travel demand and supply  fleet planning approach changes
As time progressed the importance of engineers in the decision making process reduced and introduced experts in the field of marketing and finance
  Security and safety must be at the required level – that is the imperative

## Slide 20: Experts from Marketing and Finance
The aviation market is highly volatile due to a wide range of economic, geo-political. Environment and social factors.
Airlines are required to adapt to new conditions in order to survive in a very competitive market
The airline's business is profit oriented, rather than technically oriented

## Slide 21: Teams of Experts
Successful Decision making  synergy of teams and experts
  Determine route structures
  Determine fare policy
  Create airline brand
  Control the finance
  Determine investment levels
  Determine sources of funds, and
  Manage finances

## Slide 22: Teams of Experts
Engineers are not decision makers, but play a supportive role in decision-making, as well as during the fleet planning process
  The opinion of engineers is still of fundamental importance
Planners in airlines nowadays have the role of project managers
  They choose their team and manage it
  Each member of the team is given the opportunity to participate in the decision making, giving the maximum contribution in their field

## Slide 23: Fleet Planning Approach vs. Airline Type
There are some differences in fleet planning approaches depending on the airline type
Traditional and cargo airlines
  Traditional (engineering) approach to fleet planning
  The goal is to harmonize supply and demand in the best possible way, taking into account all technical aspects
Low cost, charter and leasing companies
  It is important to consider the impact of fleet structure on the business goals

## Slide 24: Airline Fleet Characteristics
Fleet structure
  Number of different aircraft types in the fleet determines airline fleet structure
Fleet size
  Number of aircraft by different types and the total number of aircraft in the airline’s fleet represents the fleet size
The ownership structure
  Number of owned and/or leased aircraft in the fleet

## Slide 25: Fleet structure
Single fleet (homogenous)
  Only one type of aircraft
  Lower maintenance costs and lower flight crew costs
Multi fleet (heterogeneous)
  Different aircraft types in the fleet
  Enable airlines to match demand and supply more closely, increasing passenger load factors generating more revenue
Fleet structure  airline needs









## Slide 26: Fleet Size
The use of larger aircraft on slim routes will reduce aircraft utilization and increase costs










Source: Dožić and Babić (2019)

## Slide 27: Fleet Size
If the size of the aircraft is smaller than required, this will result in spill or rejected demand, i.e. loss of passengers to competitor and missing out on the revenue generation
Fleet size  airline’s requirements














Source: Dožić and Babić (2019)

## Slide 28: Fleet Ownership Structure
Owned aircraft
Leased aircraft

## Slide 29: Fleet
Indicators of aircraft utilization
  Passengers load factor (PLF)
  Annual flight hours
Higher PLF and higher flight hours  higher revenue
Direct economic impact on revenue and costs  successful business of an airline
Fleet structure, fleet size and fleet utilization  profitability
Fleet  market requirements

## Slide 30: Fleet
Average price of new aircraft (millions of US dollars)
  70.1 – 403.9 Airbus
  74.8 – 351.4 Boeing
  20-50 – smaller, regional aircraft
With slim profit margins, airlines are always looking for ways to make marginal gains from their fleets.

## Slide 31: Levels of Fleet Planning
Strategic level
Tactical level
Operational level

## Slide 32: Strategic Level
What should be considered?
  Long-term business strategy of an airline
  Economic development
  Legislation
  Development strategy of airports which airline will operate in the future
  Aircraft manufacturers with their products
Strategic decisions are long-term decisions

## Slide 33: Tactical Level
Refers to decisions related to aircraft acquisition based on
  Fleet commonality
  Aircraft price
  Route network (hub and spoke or point to point)
Decisions are mid-term or short-term

## Slide 34: Operational Level
Related to fleet assignment, i.e. assign aircraft to legs for each day of the week
Decisions are short-term

## Slide 35: Fleet Management
Fleet management
  Broader than fleet planning
  Fleet planning is a part of fleet management (mostly related to aircraft acquisition)
  Aircraft acquisition and financing
  Tactical fleet management
  Asset value maintenance
  Aircraft trading

## Slide 36: Aircraft acquisition
Two main reasons for aircraft acquisition
  Replacement of existing capacity because of inappropriate characteristics, and more effective and efficient aircraft with the same mission added to the fleet
  Capacity growth could be growth within the existing network driven by the increase of demand and could be induced by introducing a new service

## Slide 37: Aircraft Evaluation
The expertise involved
  Different education – different perspective
Obtaining airline-specific data
  Network, route, airport, current fleet, product requirements
Marketing analysis
  Demand, traffic and revenue forecast
Technical analysis
  Design, safety, reliability, maintainability, aerodynamics, stability and control, internal/external noise, emission...
Performance analysis
  Payload-range diagrams
Cost analysis
  Capital costs, DOCs
Power plant analysis
  Thrust, specific fuel consumption, fuel-burn...
Avionics
  Standard avionics, buyer-furnished avionics
Options and customization
  Standard specification, seller-furnished equipment, buyer-furnished equipment
Customer support analysis
  Initial provisioning, training and technical support, warranties and guarantees
The fleet commonality issue
  Aircraft assignment, aircrew training and rostering flexibility, inventory and type-specific ground support equipment, training and rostering of maintenance personnel
Other considerations
  Timing, financial support, single/multi-fleet
Pricing and economic analysis
Contracting

## Slide 38: Fleet Planning
Air travel demand increase
Changes in fleet size/structure
Aircraft acquisition
Buying or leasing
Appropriate methodological approach
Corresponding fleet selection
Permanent fleet management
Airline
Profit
Passengers’ interests
Airline’s interests
Operational requirements

## Slide 39: Complexity of Planning
In order to complete the airline’s mission in the market:
  consider both passengers’ and their own interests
  satisfy different operational requirements and
  ensure profitability
As growth in air travel passenger demand is expected to more than double in the next two decades, airlines need to adjust the capacity they offer
In order to accommodate rising demand, changes in fleet size/structure are needed
Airlines may need to acquire additional aircraft and make decisions whether to buy or lease new aircraft

## Slide 40: Main Reasons for Aircraft Acquisition
  Replacement of existing capacity
    Inappropriate characteristics, and
    More effective aircraft which will have the same mission should be replace older aircraft in the fleet
  Capacity growth
    Growth within the existing network driven by the increase of demand, and
    Induced by the introduction of a new service

## Slide 41: Aircraft Finance
An important factor when assessing:
  the investment
    which aircraft should be acquired and at what cost?
  financing
    how should the acquisition be financed?
  Holloway (2008)

## Slide 42: Aircraft Finance
  Main sources of finance
  From the airline’s own capital funds
  A combination of internal funds and debt
  Leasing options
An airline could own aircraft or could lease aircraft
The ratio owned/leased aircraft should be determined in a way that enables an airline to increase profitability and reduce the costs

## Slide 43: Aircraft Lease – definition
An aircraft lease – a contract whereby the owner of an aircraft (the lessor) grants to another party (the lessee) the exclusive right to the use of the aircraft for an agreed period, in return for the periodic payment of rent (the fee)
(Morrell, 2013)

## Slide 44: Airline Fleet Ownership Structure Analysis
Airline business model
  Full service and low-cost airlines
Geographic distribution
  European and North American airlines
According to total fleet size airlines were divided into three categories
  Large (more than 100 aircraft)
  Medium (from 50 to 99 aircraft)
  Small (less than 50 aircraft)

## Slide 45: Ownership structure
Airlines’ size | Number of airlines | Total number of aircraft | Total number of leased aircraft | Total percentage of leased aircraft | Average percentage of leased aircraft
Large (>100) | 43 | 11603 | 3484 | 30 | 36
Medium-large (75-99) | 15 | 1244 | 454 | 36 | 37
Medium-small (50-74) | 22 | 1295 | 754 | 58 | 58
Small (<50) | 52 | 1240 | 770 | 62 | 63
Data source: https://www.planespotters.net/airlines

## Slide 46: Findings
Airline business model’s do not significantly affect fleet ownership structure
European airlines prefer to lease aircraft compared to North American airlines
A small number of aircraft in an airline’s fleet (less than 50) implies higher percentage of leased aircraft (more than 50% of the fleet is leased)
Larger numbers of aircraft in an airline’s fleet (more than 100) implies smaller percentage of leased aircraft (on average, approximately one third of the fleet is leased)
Membership of an alliance does not affect the fleet’s ownership structure
Average total percentage of leased aircraft increase as the fleet size decrease.

## Slide 47: Why is that important?
Airlines
  An ownership structure analysis and summary of all data related to previous experiences of different airlines
  Lease or buy an aircraft
Leasing companies
  Define a target group of airlines to whom they could lease corresponding aircraft in appropriate time

## Slide 48: Further reading
Clark, P. 2007. Buying the big jets: Fleet planning for airlines, second edition, published by Ashgate Publishing Limited, England and Ashgate Publishing Company, USA.
Dožić, S., Babić, D. 2019. Airline fleet and netwoerk planning, University of Belgrade – Faculty of Transport and Traffic Engineering (ISBN 978-86-7395-407-3). Handouts in Serbian language
Dožić S., Kalić М. 2015. Three Stage Airline Fleet Planning Model, Journal of Air Transport Management, Vol 46, pp. 30-39.
Dožić S., Krnić R. 2016, Overview of airline fleet ownership structure, XV international symposium Symorg 2016, Zlatibor, Serbia, June 10-13, pp. 854-862. (ISBN: 978-86-7680-326-2) (Session International Management: http://symorg.fon.bg.ac.rs/proceedings/2016/papers.html)
Dožić S., Lutovac T., Kalić М. 2018. Fuzzy AHP approach to passenger aircraft type selection, Vol. 68, pp. 165-176.
Holloway, S. 2008. Straight and Level – Practical Airline Economics, 3rd Edition, Ashgate
Morrell, P. 2013. Airline Finance, 4th Edition, Ashgate

## Slide 49
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com