## Slide 1: Airline Planning and Operations Schedule planning
Danica Babić
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Schedule design
2

## Slide 3: Flight Schedule Planning
Flight schedule design
Optimal number of flights
Aircraft assignment
Assign the right aircraft type to each flight in the schedule
Aircraft routing
Aircraft utilisation optimisation
Crew Scheduling
Crew utilisation and cost optimisation

## Slide 4: Stages in the Flight Schedule Planning Process
60+ months
Long range planning
36-12 months
Market evaluations
12-6 months
Flight schedule optimization
4-1 months
Flight schedule operational changes
Fleet diversity
Labor planning
Hub development
Add/change hub
Appropriate facilities and equipment at airports
Airport Infrastructure
Frequencies and departure times
Expand/shrink markets
Price policy
Predicting competitor behavior/modelling
Code-sharing and alliance
Initial flight schedule for available fleet
Fleet assignment
Evaluating facilities and manpower capabilities
Crew scheduling
Arrival/departure times
Maintenance

## Slide 5: Flight Schedule Definition
Flight schedule contains the following information:
  Day of the week
  Airport and time of departure
  Airport and time of arrival
  Number of intermediate stops
  Aircraft type
  Flight number
  Transfer information
Flight schedule is the result of offered capacity by an airline, on the one hand, and passenger demand, on the other hand, while satisfying a number of restrictions

## Slide 6: Some Definitions….
Airline base airport – an airport at which the airline has its registered office
Airlines can have multiple bases
After deregulation, airlines tend to have one base for each type of aircraft in the fleet
Aircraft rotation (or aircraft routing) - a series of flights such that the first flight in a row starts from the base, and the last flight ends at the base of the airline (flights are performed by one aircraft).
Rotations can be defined as daily or multi-day.

## Slide 7: Flight Schedule Design
Flight schedule design - determination of departure times for all destinations across the network in response to the economics of supply and taking into consideration operational constraints.
An airline’s success (revenue, quality of service, etc.) depends on the schedule design (criteria and restrictions) and effective execution of the schedule (reliability and robustness).
One of the most complex tasks faced by an airline (combinatorial problem) and it is important to meet:
    Airline needs
    Passenger needs
    Technical constraints
    Legal restrictions
    Geo-political considerations

## Slide 8: Airlines vs. Passengers
Airlines
High load factors per flight
Passengers
Non-stop flights
High aircraft utilization
Low operating costs
Maximized revenue
High frequency per route
High network connectivity
Departure timings adjusted to passenger preferred departure time
Low connecting times at hubs
High seat availability

## Slide 9: Technical (operational) and Legal Constraints
Flight schedule
Airport slots
Ground handling time
Maintenance
Fleet
Passengers
Competition
Routes
Crew
Time zones
Weather conditions

## Slide 10: Flight Schedule Design – An Iterative Process
Flight schedule
Fleet assignment/
Aircraft routings
Crew scheduling
Crew rostering
Disruptions in
flight schedule
execution
Planning stages
Operational phase
Routes and frequencies
Employment/union
contractsand rules
Maintenance

## Slide 11: Flight Schedule Types
Official flight schedule
Operational flight schedule
Daily flight schedule
Commercial Office
Operations Center – Operation plan
Operation Center – Schedule execution
Aircraft and crew scheduling
Destinations
Frequencies
Departure/Arrival time
Traffic monitoring
Disruption solving

## Slide 12: Fleet assignment
12

## Slide 13: Flight Schedule Design
Flight schedule
Route selection
Schedule design
Aircraft assignment
Crew pairing
Crew rostering
Crew schedule
Aircraft type selection
Aircraft routing

## Slide 14: What to Consider when Designing an Aircraft Assignment Plan?
Initial flight schedule  assign the appropriate aircraft type to each flight in the schedule
The task of aircraft assignment is to match each aircraft type in the fleet with a particular route in the schedule in terms of:
  Capacity vs demand
  Operating costs vs revenue
  Maximum Take-off Weight
  Turnaround time
The goal of aircraft assignment is to assign as many flight segments as possible in a schedule to one or more aircraft types, while optimizing some objective function and meeting various operational constraints

## Slide 15: Time-Space Network
Time-space network
  Nodes:
    Departure/arrival airport (time and space)
  Links:
    Flights: each link represent one flight
    Turnaround time
8:00
12:00
16:00
20:00
8:00
12:00
16:00
20:00
A/p A
A/p B
A/p C
A/p D

## Slide 16: Aircraft Assignment Problem
Assign the right aircraft type to each flight in the schedule by taking into account:
  Fleet heterogeneity (different capacities)
  Only one aircraft should be assigned to each flight
  The required number of aircraft is not greater than the number of available aircraft in the fleet
  The airport where the aircraft must end its rotation (aircraft balance)
Airline goals:
  Profit maximization
  Cost minimization
  Minimum number of aircraft required
  Maximum number of connections
  Additional constraints: aircraft range, noise restrictions...

## Slide 17: Objective Function: Minimum Cost of Assigning Aircraft on Routes
Cost = operating costs + spill costs
Operating costs = CASM of aircraft type x distance x number of seats
Route length – 2475 miles
Operating costs B737-800 = $0,042 x 2475 x 162 = $16 840
Operating costs B757-200 = $0,044 x 2475 x 200 = $21 780
Aircraft type | CASM ($) | RASM ($) | No of seats
B737-800 | 0,042 | 0,15 | 162
B757-200 | 0,044 | 0,15 | 200

## Slide 18: Spill Costs
Depend on passenger demand
B757-200 rejected passengers
B737-800 rejected passengers
162
200
µ=150
N=(150,30)
Expected spill costs = expected number of spill passengers x distance x RASM

## Slide 19: Spill Costs
Expected number of spill passengers for B737-800 = 6,91
Expected number of spill passengers for B757-200 = 0,60
Expected spill costs for B737-800 = 6,91 x 2475 x 0,15 = $2565
Expected spill costs for B757-200 = 0,60 x 2475 x 0,15 = $223

## Slide 20: Retained Demand
Part of the demand that can be retained = 15%
Expected spill costs for B737-800 = $2565 x 0,85 = $2180
Expected spill costs for B757-200 = $223 x 0,85 = $189
Cost for B737-800 = $16 839 + $2180 = $19 020
Cost for B757-200 = $21 780 + $189 = $21 969

## Slide 21: Aircraft routing
21

## Slide 22: Aircraft Routing
Aircraft routing (aircraft rotation) is the process of assigning each individual aircraft (referred to as tail number) within each fleet to flight legs.
  Input: determine rotations by aircraft types from the previous phase
Airline goal: minimum cost.
Defining feasible routes for a specific aircraft type considering the requirements of maintenance action.
Main goals of aircraft routing:
  Each flight must have an aircraft assigned (tail number)
  Follow the maintenance service schedule
  Constraint: aircraft must end their day at a defined time, at a specific airport where maintenance actions will be performed.

## Slide 23: Aircraft Routing Daily Problem
The dispatcher encounters issues when allocating available aircraft to certain routes on a daily basis
A large number of options aircraft can generated for each routing
Input: Number of remaining hours that the aircraft may spend in operation before going to the mandatory technical inspection at the base
Airline goal: Maximum possible operation of individual aircraft before a return to base

## Slide 24: Solving the Problem of Aircraft Routing
Input
  Remaining number of hours of individual aircraft from the fleet during which the aircraft can be in operation before leaving for the technical base
  Average daily flight hours per aircraft, maximum time between two consecutive maintenance service
Output
  The latest date by which the aircraft can remain in service
Goal
  Minimize the total number of unused hours that all aircraft in the fleet could spend in operation before returning to base

## Slide 25: Dichromatic graph
Available aircraft
Routes
T
S
t1
t2
t3



ti
tm









s1
s2
s3
si
sm
Going to base
Going to base
Route duration
Unused hours
Four sets of aircraft:
  Great than one day
  Just over a day
  One day
  Several hours

## Slide 26: Crew scheduling
26

## Slide 27: Crew Scheduling
Crew scheduling involves the process of identifying sequences of flight legs and assigning both the cockpit and cabin crews to these sequences.
Crew utilization importance  total crew cost, including salaries, benefits, and expenses, presenting the second largest cost element, after the cost of fuel, for airlines.
Crew utilization depends on flight schedule design
Crew scheduling process:
  Crew pairing
  Crew rostering

## Slide 28: Crew Pairing
Crew pairing is a sequence of flight legs, within the same fleet, that starts and ends at the same crew base.
Problem definition: assign a crew to all planned tasks (flights, simulator, office work).
Objective function:
  Minimizing total crew costs, maximizing crew utilization, minimizing the number of reserve crews, etc.
Crew pairing must satisfy many constraints such as union, government, and contractual regulations.
Constraints:
  Allowed working hours, prescribed breaks between flights, daily number of take-offs and landings, reliability, etc.

## Slide 29: Crew Pairing Issues
Crew pairing determination for a given flight schedule:
  All flights must have an assigned crew
  Minimizes the total crew cost
  Satisfy the regulations and flight time limitiations
  Crew pairing - ususal duty of one to five days
The final crew pairing includes dates and times for each day.

## Slide 30: Elements of crew pairing
Set of flights
Crew tasks

## Slide 31
Airline
base airport
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
leg
Duty time
Rest time
Rotation I
Rotation II
leg
leg
leg
leg
Time between two flights
Rotation III
leg
leg
leg
leg

## Slide 32: Regulation Official Journal of the European Union / FAR (USA)
Maximum working hours - 11 h to 14 h, depending on the number of take-offs/landings
The minimum rest period - 8 hours to 6 hours has no duties assigned
Sit connection: Time between flights during working hours (includes waiting time, changing aircraft, 10 minutes to 3 hours)

## Slide 33: Crew Rostering
Crew rostering is the process of assigning individual crew members to crew pairings, usually on a monthly basis.
Factors affecting rostering: crew training days, seniority, vacation period, days off, medical examinations, flight revalidations etc.
Crew rostering should be made so that all pilots have approximately the same number of days on duty and the approximate number of days off.
1 2 3 4 ... 30
Training days
Days off
Medical examinations

## Slide 34: Elements of Crew Scheduling
Set of flights
Crew tasks
Crew pairing
Crew rostering

## Slide 35: Crew Rostering
Objective functions:
  Minimum deviation between the average monthly flight hours per crew member and the actual monthly flight hours per crew member
  Minimum deviation between the average number of days on duty during the month and the actual number of days on duty per crew members
  Minimum combination of deviations related to monthly flight hours and deviations related to the number of days on duty
  Minimum overtime costs
  Minimum number of pilots who have monthly flight hours less than guaranteed

## Slide 36: Mathematical model
m – the number of crew members to be deployed
n – the number of rotations assigned to the crew members
m  n
cij – The cost of assigning pilot i to the rotation j

## Slide 37: Literature
Bazargan, M., Airline Operations and Schedul-ing. 2nd Hrsg. Burlington: Ashgate Publishing Company, 2010.
Barnhart, C., Johnson, E., Nemhauser, G.L., and Vance, P.H. (1997). Airline crew scheduling: A new formulation and decomposition algorithm. Operations Research, 45 (2), 188–200.
Holloway, S., 2003. Straight and Level: Practical Airline Economics, Ashgate Publishing Limited. Gower House, Croft Road, Aldershot, Hampshire GU11 3HR, England.
Jarrah, A., Goodstein, J., and Narasimhan, R. (2000). An efficient airline refleeting model for the incremental modification of planned fleet assignments. Transportation Science, 34 (4), pp. 349–63.
Sherali, H. D., Bish, E. K., and Zhu, X. (2006). Airline fleet assignment concepts, models, and algorithms. European Journal of Operational Research, 172 (1), pp. 1–30.
Talluri, K. (1998). The four-day aircraft maintenance routing problem. Transportation Science, 32 (1), pp. 43–53.
Wensveen, J. 2015. Air Transportation: A Management Perspective. Publisher: Routledge; 8th edition.

## Slide 38
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com