## Slide 1: Airline Planning and Operations Airline operational control
Slavica Dožić
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Flight planning
2

## Slide 3: Design of Flight Schedules
Flight schedule design is a procedure that requires determining departure times for all destinations on the network, optimizing the objectives within the given constraints
Very complex, combinatorial problem
Operational success of an airline (income, quality of service, etc.) depends on the design and execution of the flight schedule
During the planning process, the flight schedule is designed to fulfill passenger demand, turn a profit and satisfy different operational requirements

## Slide 4: Daily Operational Flight Schedule
Many unforeseen events can cause unexpected fluctuations and changes in the flight schedule for the airline.
Such disturbances make it challenging to maintain the planned flight schedule. The operational airline dispatcher adjusts or creates a new daily operational flight schedule
The daily schedule is the final version of the flight schedule for any given day, which takes into account all the changes that were undertaken during the period from its publication (flight schedules are usually issued several months in advance and cover a period of one season, i.e. 6 months).

## Slide 5: Daily Operational Flight Schedule
The daily schedule is a set of aircraft and crew (flight and cabin) routings for a one-day time period handed to the dispatchers at the airline operations control centre in charge of its implementation.
Depending on airline policy, when designing the daily operational flight schedule, the dispatcher delays or cancels some flights and reassigns flights to available aircraft in order to reduce the negative effects of changes.

## Slide 6: Planning Process
Flight schedule
Aircraft rotations
Crew rostering
Fleet assignment
Crew pairing
Optimal flight schedule
(Dream)

## Slide 7: Influences on Planned Flight Schedule and Consequences
Planned flight schedule
Crew absence or delay
Meteorological conditions
Reality
Flight delay
Missed connection
Spare crew
Ferry flight
Irregularity during passenger boarding or baggage processing
Aircraft failure
Errors in estimation of time
Airport congestion
Air traffic control

## Slide 8: Disturbance Scheme
Meteorological conditions
Aircraft failure
Crew absence or delay
Errors in estimation of block or turnaround time on some airports
Airport congestion
Air traffic control
Irregularity during passenger boarding or baggage processing
Aditional costs
Passenger’s loyalty
Reducing airline’s reputation
Flight schedule disturbances
Planned flight schedule
New daily operational flight schedule
Delay and/or cancellation of certain flights

## Slide 9: Disturbances – Classification
Disturbances
Internal
Crew delay or crew absence
Aircraft failure
External
Meteorological conditions
Airport or airspace congestion

## Slide 10: Mitigating Strategies Used By Dispatchers?
Flight delaying
Aircraft swapping
Flight cancellation
Ferry flight
Introducing spare aircraft

## Slide 11: Theoretical Airline Schedule Disturbances
Addressed in literature with several different models, objective functions, constraints and assumptions, as well as different solution approaches
Goals
  Establish the traffic in accordance with the planned flight schedule as soon as possible
  To reduce the impact of perturbations on income or to reduce the total or additional costs induced by perturbation

## Slide 12: What is the Objective Function?
Recovery period minimization
Cost minimization
Profit maximization
Delay minimization
…

## Slide 13: Solving the Flight Schedule Disturbance Problem
Software solving the problem in real time
Decision Support System
Interactive

## Slide 14: Objective
To develop software with a user friendly interface, as a decision support tool for the dispatcher in AOC
To develop the mathematical model and heuristic algorithm for handling schedule perturbations and redesign of the flight schedule

## Slide 15: Problem Definition
For a planned daily flight schedule under conditions when perturbations have occurred, one has to design a new daily operational flight schedule that will minimize additional costs and disruptions to the airline

## Slide 16: JAT Airways’ Decision Support System (ASO Simple)
Developed by UB-FTTE

## Slide 34: ASO Advanced Decision Support System
Developed by UB-FTTE

## Slide 35
Mathematical model
Heuristic procedure
ASO Advanced
Objective function
Revenue
Costs (penalties)
Goals
Interest
direct operational costs
flight delay cost
non-priority flight cancellation cost
aircraft maintenance disturbance cost
priority flight cancellation cost
aircraft balance disturbance cost
Assumptions
Constraints

## Slide 36: Problem Definition
For a planned daily flight schedule for an airline under conditions when a disturbance has occurred, one has to design a new daily operational flight schedule that will maximize profit for the airline

## Slide 37: Airline Policy
The main actions when solving problems due to disturbances:
    Flight cancellation
    Flight delaying
    Resource (aircraft) substitution
Without usage
    Spare resource
    Ferry flights

## Slide 38: Example
Aircraft AT7-YUALO has a technical problem. The aircraft has a planned repair schedule from 10:50 till 18:00 h.

## Slide 44: Conclusions
Decision support tools with user friendly interface for solving airline schedule perturbation problems in operational real time
Potential Solutions sorted in priority of increasing value of the objective function is offered to decision maker
New strategies can be defined by changing values of penalties (costs), therefore the DSS can accommodate different airline policies

## Slide 45: Further reading
Babić, O., Kalić, M., Pavković, G., Dožić, S., Čangalović, M. 2010. Heuristic approach to the airline schedule disturbances problem, Transportation Planning and Technology, Vol. 33, No. 3, pp. 257-280. https://doi.org/10.1080/03081061003732318.
Belobaba, P., Odoni, A., Barnhart, C. 2009. The global airline industry, John Wiley & Sons.
Dožić, S. 2007. Models to Solve Airline Schedule Perturbation Problem, master thesis, defended in October 2007 at the University of Belgrade – Faculty of Transport and Traffic Engineering.
Wensween, J. 2007. Air Transportation: A Management Perspective, 6th Edition, Ashgate.
Project Airline Schedule Optimisation, Institute of the UB-FTTE, Belgrade, 2002 – 2004. (Clients: Ministry of Science and Environmental Protection of Republic of Serbia and JAT Airways)

## Slide 46
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com