## Slide 1: Airline Planning and Operations Air cargo
Radosav Jovanović
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only.
The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com

## Slide 2: Definitions – Basic Terms
Air cargo or freight refers to any property carried on an aircraft other than mail, stores and passenger baggage (ICAO)
Air Freight = (typically) commercial goods transported by plane
Air Cargo = any property (i.e. air freight + mail + express shipments) transported by air except baggage
ATK = available tonne-kilometres . The number of tonnes of capacity available for the carriage of revenue load (passenger and cargo) multiplied by the distance flown.
FTK = freight tonne-kilometres – measure of performed transport work. The number of revenue tonnes of cargo (freight and mail) carried multiplied by the distance flown. (E.g. carrying 10t of freight over 1,000km generates 10,000 FTK)
RTK = revenue tonne-kilometres = measure of the carrier’s output actually sold = the revenue load in tonnes multiplied by the distance flown in km.

## Slide 3
Period | World GDP | Freight Tonne Km
1960-1969 | 4.8 | 17.8
1970-1979 | 3.6 | 10.9
1980-1989 | 2.4 | 7.9
1990-1999 | 2.6 | 7.3
2000-2009 | 2.9 | 5.0
2010-2019 | 2.95 | 2.1
World Economic and Air Cargo Growth
Average annual growth rates (%)
Chart: Freight tonne-kilometres (millions)
| 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
 | 15568.7001 | 16955.1999 | 17236.2001 | 19300.3004 | 21322.8001 | 23579.8998 | 25626.6997 | 26825.2004 | 28360.5003 | 29046.2998 | 32407.8999 | 36841.9996 | 37061.7002 | 40331.8001 | 45392.7001 | 50418.6 | 54428.2003 | 56124.9004 | 56142.3001 | 61025.1997 | 67522.6002 | 77183.3003 | 83098.2004 | 89164.6 | 102876.1012 | 101788.2743 | 108629.6182 | 118257.211 | 110860.835 | 117506.673 | 124203.199 | 139032.94 | 141483.603 | 148937.604 | 158205.946 | 158487.874 | 175509.3437 | 182025.6271 | 183037.2301 | 175051.3422 | 175829.5578 | 184831.1095 | 187769.4163 | 194898.2751 | 212866.6472 | 221165.7008 | 215169.2354

## Slide 4: Freight vs. Passenger Traffic (RTK split) World, 2019 data, scheduled services
Passengers :
  4.5 billion passengers
  8,686 billion passenger-km
Air freight:
  57.6 million tonnes of air freight carried
  225 billion FTK
Air mail: 6.8 billion of mail tonne-km
Passengers + cargo:
  1,042 billion RTK
=> Air cargo (freight + mail) represented about 22% of total scheduled air transport in 2019, measured in tonne-kilometres

## Slide 5: Role of Air Cargo -Economy
Global Value Chains = complex, interlinked networks of cross-border and domestic flows of goods, services, capital and labour. They rely on the ability to move goods quickly, cost effectively, and reliably across borders.
Airlines transport over 58 million metric tonnes of goods a year, representing more than 35% of global trade by value but less than 1% of world trade by volume.
That is equivalent to $6.8 trillion worth of goods annually, or $18.6 billion worth of goods every day.

## Slide 6: Example Global Cargo Supply Chains

## Slide 7: Nature of Demand for Air Cargo
Emergency goods, e.g.
  Human organs for transplantation
  Vaccines
  Spare parts of machines (esp. when production bottlenecks)
  Documents (less so nowadays due to e-signatures)
Ultra-high value goods, e.g.
  Diamonds
  Jewellery
  Works of art
Perishable goods, e.g.
  Agricultural products (food)
  Pharmaceutical products
  Fashion garments
Routine, non-perishable goods, e.g.
  High-value industrial products (e.g. medical technology), electronic products with high value/weight(volume) ratio (e.g. mobile phones, tablets, cameras, etc.), Just-in-time distribution systems, etc.

## Slide 8: Structure of Transported Air Cargo Per Region-pair and Direction

## Slide 9: Examples of Frequently Air-freighted Goods
Source: Shepherd et al., 2016, p15.

## Slide 10: Cargo Handling Classification
General cargo – ordinary shipment items; does not normally require special handling. Examples: household goods, office equipment, sports equipment, clothing (garment, textiles), etc.
Special cargo – because of its nature and/or value requires special treatment: handling procedures, ambiental characteristics, etc. Further classified as:
  Perishable cargo (load information code: PER)
  Valuable goods (VAL)
  Dangerous goods (DGR)
  Live animals (AVI)
  Heavy / oversized cargo (HEA/BIG)
  Human remains (HUM)
  Diplomatic cargo/mail (DIP)
  Vulnerable cargo (VUN)
  Service cargo (AOG)
  Express shipments (XPS)

## Slide 11: Special Cargo – Rules and Regulations
Special cargo handling addressed in international, national regulations and company rules & manuals
ICAO Annex 18: Technical instructions for the carriage of dangerous goods by air
IATA manuals:
  Dangerous Goods Regulations (DGR)
  Perishable Cargo Regulations (PCR)
  Temperature Control Regulations (TCR)
  Live Animals Regulations (LAR)
  …
National legislations
Company (airline) rules
  Ground Operations Manual (GOM) – compliant with IATA manuals or more restrictive

## Slide 12: Air Cargo Capacities – Options
Hold of passenger aircraft (i.e. pax on main deck; baggage and cargo on lower deck)
All-cargo (freighter) aircraft ( converted passenger aircraft) – cargo on both decks
Combi-aircraft (both cargo and passengers on main deck, in separate compartments; baggage and cargo on lower deck)
55-60% of FTK carried on freighter aircraft, the remaining part in bellyholds of passenger aircraft
Widebody freighters represent vast majority of cargo capacity (in ATK)

## Slide 13: Holds of Passenger Aircraft – Indicative Cargo Capacities
 | Payload remaining, assuming max. passenger load (t) | Cargo volume (m3)
A320 | 1 | 3.6
B737-300 | 2.3 | 21
B737-400 | 2.9 | 24
B737-800 | 3.6 | 28
A330-200 | 14.1 | 61.8
A330-300 | 15 | 80.2
B767-300 | 16.5 | 63
B747-400 | 20 | 73.4
A380 | 20 | 68
Narrow-bodies
Wide-bodies

## Slide 14: Freighter Aircraft Capacities
A/c type | Max. payload (t) | Cargo hold volume (m3) | Main deck cargo door size (W x H, cm)
B757-200F | 32.8 | 187 | 340 x 218
A300-600F | 54.6 | 310 | 360 x 260
B777F | 103.7 | 580 | 372 x 305
AN-124 | 120 | 900 | 640 x 440
B747-8F | 134 | 858 | 340 x 305*
B747 cross-section

## Slide 15: Most Commonly Used Freighter Aircraft
Wide-bodies
Narrow-bodies

## Slide 16: Unit Load Devices (ULD)
ULD = an assembly typically comprising an aircraft container, an aircraft pallet and pallet net.
Purposes:
  Secure the loads during flight
  Eliminate loose loading and unloading of aircraft holds
  Protect the contents
  Maximize the use of aircraft contour
  Allow fast and easy transfer from one aircraft to another
  Special-purposes ULD (e.g. animals, with temperature control, etc.)

## Slide 17: ULDs – Containers and Pallets
Frequently used lower-deck containers
Example main-deck container
PGE pallet (main deck)

## Slide 18: Air Cargo Supply Chain: Flow of Goods

## Slide 19: Flow of Goods and Information / documentation
Source: Ehrler, V.

## Slide 20: Key Actors Involved in Air Cargo Supply Chains
Consigner (shipper) - person or company that has issued the contract for carriage (i.e. the “air waybill” – see later) of the goods.
Freight forwarder – an intermediary, who acts on behalf of importers, exporters and other companies or persons involved in shipping goods, organising safe, efficient and cost-effective transportation of goods. Freight forwarders arrange the best means of transport, using the services of shipping lines, airlines, road and rail freight operators or/and own fleet.
Ground handler - a company specialised in loading and unloading cargo from aircraft and building and breaking down ULDs.
Air cargo carrier – a company that flies cargo from one airport to another using aircraft*.
Consignee - the person or company whose name appears on the air waybill as the party to whom the goods are to be delivered by the carrier, or the receiver of the shipment.

## Slide 21: Transport Supply – Air Cargo Carriers
Three basic categories:
  Combination carriers – carrying both passengers and cargo; includes all except low-fare airlines
  Non-integrated cargo-only airlines, e.g. Cargolux, Nippon Cargo Airlines
  Integrated cargo-only carriers (“Integrators”) – focusing on smaller consignments, integrating the roles of freight forwarders and carriers, e.g. FedEx, UPS, DHL
Izvor: SDG

## Slide 22: Largest Air Cargo Operators
Source: Airline Business
Top 25 air cargo operators by traffic, 2018

## Slide 23: Structure of Transport Chains
INTEGRATOR
ALL-CARGO CARRIER
SHIPPER
FREIGHT FORWARDER
COMBINATION CARRIER
CONSIGNEE
FREIGHT FORWARDER

## Slide 24: 1. Combination Carriers
Hundreds of carriers which transport both passengers and cargo
Cargo is often a by-product (but there are exceptions!)
Source: Flight Airline Business
Carrier | Cargo revenue as share of total revenue, 2016
Air France | 8%
British Airways | 5%
China Airlines | 28%
Korean Air | 21%
Cathay Pacific | 22%
Emirates | 12%
Qatar Airways | 17%
Delta Air Lines | 2%
American Airlines | 2%

## Slide 25: 2. Non-Integrated Cargo-only Carriers
More flexible than combination carriers concerning airport choice and departure times.
Business models:
Full all-cargo carrier. Own fleet, carrying solely cargo (primarily “standard” shipments). Examples: Cargolux, Nippon Cargo Airlines, AirBridgeCargo
ACMI operator. Aircraft, Crew, Maintenance, Insurance. Leasing out their fleet and crew. Example: Atlas Air: wet-lease. Fleet: ≈40xB747F, ≈30xB767F, ≈10xB777F, ≈10xB737F.
3. Specialised cargo carriers (Niche carriers). Specialised for cargo transport which requires special equipment. Example: Volga-Dnepr Group (2016: 12xAN-124-100, 5xIL-76TD-90VD).

## Slide 26: 3. Integrated Cargo-only Carriers (“integrators”)
Performing their own pickup and delivery services of smaller parcels, operate aircraft and trucks to support door-to-door delivery operations supported by advanced information and communications technologies.
Predominantly B2B demand (...)
Key elements of the business model:
  Door-to-door service,
  Guaranteed delivery time
  Continuous tracking of the shipment
  Multimodal network and fleet (aircraft, truck, van)
  Night operations (hub/feed model)
  Secondary airports with strong regional demand as network hubs (Memphis, Louisville, Leipzig, Liege, Cologne/Bonn, East Midlands,...)
  Focus on high-yield (premium) services
FedEx, UPS, DHL

## Slide 27: Freight Forwarders
To the airlines the freight forwarder is the shipper, and to the shipper an indirect carrier or agent.
The forwarder
  receives freight from the shipper under his own tariff, often consolidating it into larger shipments (to obtain better rate),
  prepares the necessary documentation, and
  delivers it to the airline, sometimes in aircraft-compatible ULDs.
Bridging gap between airlines and consumers – “architects of transport chains”
Severe competition between airlines for business of a few powerful forwarders
2019 rank | Freight forwarder | Air cargo (Metric tonnes)
1 | DHL Supply Chain & Global Forwarding | 2,051,000
2 | Kuehne + Nagel | 1,643,000
3 | DB Schenker | 1,186,000
4 | DSV | 1,071,266
5 | UPS Supply Chain Solutions | 965,700
6 | Expeditors | 955,391
7 | Nippon Express | 752,942
8 | Sinotrans | 502,000
9 | CEVA Logistics | 416,000
10 | Kerry Logistics | 409,408

## Slide 28: Key Documents
Air waybill (AWB). A document prepared by or on behalf of a shipper that evidences the contract between the shipper and aircraft operator(s) for the carriage of goods for the routes of the operator(s). AWBs have several purposes, but their two main functions are:
  contract of carriage (behind every original AWB are the conditions of contract for carriage), and as
  evidence of the receipt of goods.
An AWB is the most important document issued by an aircraft operator either directly or through its authorized agent (freight forwarder), and covers the transport of cargo from airport to airport.
Air cargo manifest. A document issued by an aircraft operator, containing the details of consignments loaded on to a specified flight. It provides a list of all the AWB numbers referring to the goods loaded on to an aircraft. The nature of the goods, weight, and number of pieces composing each consignment on a specified flight, and the unit of loading used, are also identified in this document.

## Slide 29: Directional Imbalances
Source: IATA Annual Review 2019

## Slide 30: Polygonal Routes as a Solution

## Slide 31: Air Cargo Tariffs / Rates
In the past Air Services Agreements usually included a restrictive tariff clause that required the airline to submit its cargo rates to the authorities in both origin country (i.e. its own government) and the destination country for approval. The business matter is discussed at IATA Cargo Tariff Coordination Conferences
Nowadays, the IATA-coordinated rates have largely been replaced by contract rates by most major network airlines. IATA tariffs are increasingly ignored on many of the major routes due to competition, however, still relevant for many less developed markets and continue to provide a general guideline.
Still, the Air Cargo Tariff (TACT) document contains the detailed record of all cargo rates and rules that are agreed by airlines and is published by IATA three times a year. It contains the following rates:
  general cargo rates
  specific commodity rates
  class rates (commodity classification rates)

## Slide 32: Air Cargo Rates
General cargo rates (GCR) apply to the carriage of commodities in general, i.e. for goods that have not been allocated a specific commodity rate or class rate; General commodity shipments are rated by weight., e.g.:
  Less than 100kg = Normal GCR (GCR N)
  More than 100kg = Quantity GCR (GCR Q)
  There is generally a minimum charge (M), depending on the city-pairs between which the shipment takes place. London – New York example.
Specific commodity rates relate to the carriage of particular commodities from a specified point of origin to a specified destination point; they are designed to encourage certain types of cargo (e.g. food stuffs, fruite and vegetables, etc.) to be air freighted and are usually lower than GCR.
Class rates (commodity classification rates) are published for particular commodities from a specified point of origin to a specified destination point. They are applied to such shipments as live animals, valuable cargo, dangerous goods, perishable goods, baggage shipped as cargo, newspapers, and human remains.
LON / NYC
M…… 50 £
N……. 4.03 £/kg
Q100…. 2.15 £/kg
Q300 …. 1.34 £/kg
Q500 …. 1.24 £/kg
ULD rate..0.95 £/kg

## Slide 33: Chargeable Weight
TACT rules, section 3.9.3, chargeable weight
Chargeable weight of the shipment is the highest of the three:
  Actual gross weight
  Volumetric weight
  Minimum weight for the given tariff
Volumetric weight – used for low-density shipments, i.e. where density (mass divided by volume) is less than 167 kg/m3 (equivalent to 6,000 cm3 per kg). Thus any shipment with a density below 167 kg/m3 will be converted to a chargeable weight using this density and not its actual density.

## Slide 34: Cargo Charge Calculation Example
Routing: London (UK) to New York (USA)
Commodity: Children toys
No of pieces: 2 boxes
Gross actual weight: 5.2 kg
Dimensions: 10cm x 60cm x 30cm x 2
Volume 10 x 60x 30cm x 2 = 36,000cm3
Volumetric weight: 36,000cm3 : 6,000 cm3/kg = 6kg (> gross actual weight)
Chargeable weight: 6 kg
Applicable rate: GCR N = 4.03 GBP per kg
Weight charge: 6 kg x 4.03 GBP/kg = 24.18 GBP.
Minimum charge London – New York: 50.00 GBP. Applies!

## Slide 35
Morrell, P., “Moving boxes by air”. 2nd ed. Routledge. 2020.
Sales, M. “The Air Logistics Handbook. Air freight and the global supply chain.” Routledge. 2013.
ICAO and WCO, “Moving air cargo globally. Air cargo and mail secure supply chain and facilitation guidelines”. 2nd ed.
Shepherd, B. et al. for IATA, 2016. “Value of air cargo: Air transport and global value chains.”
Steer Davies Gleave. 2010. Air Freight: Economic and Environmental Drivers and Impacts.
https://www.iata.org/en/programs/cargo/
Further reading

## Slide 36
Introductory lecture provided by the Engage KTN
Non-commercial use only. These lecture slides are provided for not-for-profit, educational use only. The content may not be adapted or changed, and the source must be recognised.
engagektn.com / wikiengagektn.com