## Slide 1: PhD thesis: Integrating Weather Prediction Models into ATM Planning (IWA)
Anastasia Lemetti, LIU
Supervisor: Valentin Polishchuk, LIU
Co-supervisor: Tatiana Polishchuk, LIU

## Slide 2: IWA Project
Integrating Weather Prediction Models into ATM Planning
Supported by the SESAR Joint Undertaking under the European Union’s Horizon 2020 research and innovation programme under grant agreement No 783287.
Evaluate the impact of different weather conditions on route planning in TMA and on staff scheduling at Remote Tower Center
Study optimization techniques to support efficient decision-making for aviation authorities developed by LiU together with LFV (Swedish ANSP)
Study and apply probabilistic models and the corresponding weather data
Prototype and test the mathematical tools which will help take into account the influence of bad weather conditions on the developed optimization techniques solutions

## Slide 3: Integrating Weather Impact in Air Traffic Controller Shift Scheduling in Remote and Conventional Towers
The first RTC was opened in Sweden in 2015 (Sundsvall RTC)
The Swedish ANSP Luftfartsverket (LFV) serves Sundsvall Airport, Örnsköldsvik Airport and Linköping Airport from the center
Currently all service is provided in single mode (one ATCO controls one airport)
Multiple operation is planned in Sweden, as well as in other countries

## Slide 4: Measuring Weather Impact
No good measures or classifications for weather impact on ATCOs exist
Research questions:
How do different weather phenomena impact ATCO workload at different airports?
How to quantify the weather-induced capacity reductions?
How can we integrate this impact in RTC staff scheduling?
Contributes to: safety assessment of multiple operation (required by unions and regulation bodies)

## Slide 5
Strategy Outline
To integrate weather impact into RTC staff scheduling we propose the following steps:
Identify impactful weather phenomena for each considered airport
Define threshold values for these impactful weather phenomena
Obtain weather data in form of EPS
Choose exemplary historical dates and time periods
For each airport determine the hours the airport should operate in a single mode (weather phenomena exceed the threshold values from (2))
Obtain flight movements data for all airports for the chosen dates
Get the necessary number of ATCOs for RTC staffing for each EPS member
Calculate a distribution of the necessary number of ATCOs for RTC staffing

## Slide 6
Airports
AP1
AP2
AP4
AP3
AP5
Five airports, operated remotely or planned for remote operation:
AP1: Small AP w/ low traffic, few scheduled flights per hour. Inland location north of the Arctic Circle and other 4 airports
AP2: Small regional AP with regular scheduled flights (usually open 24/7). Coastal location, north of AP3-5
AP3: Small regional AP with regular scheduled flights. Coastal location, north of AP5
AP4: Small regional AP with regular scheduled flights. Coastal location, north of AP3 and AP5
AP5: Medium-sized AP, multiple scheduled flights per hour (usually open 24/7). Coastal location in the South of Sweden, Marine West Coast Climate

## Slide 7
Structured Interview
Three ATCOs with significant operational experience + some with experience in remote towers (Two of the three worked remotely)
One ATCO answered questionnaires about AP1-AP3, one about AP3-4, one about AP5
Background information on ATCO and on the airport
Common questions on the weather at the airport
Extra controllers' tasks associated with each weather phenomenon: snow, low visibility, precipitation (excluding snow), wind and convective weather
How measured
A list of additional tasks (from Eurocontrol hazard weather assessment cards) associated with minor, moderate or severe occurrence of each weather phenomenon
ATCOs

## Slide 8
Example additional tasks due to weather:
Anticipation and condition detection, Visual observation, RWY closing and re-opening for inspection,
Change of departure/arrival RWY, Early warning to pilots, Clear arrivals to holding areas, Increased separation requirements, Increased coordination, Increased frequency occupancy time, Frequent MET reports
Controllers’ answers translated to numerical values:
Structured Interview

## Slide 9
Interview Results
We summed up the numerical values reflecting controller’s answers and divided by the number of additional tasks

## Slide 10
Weather Intensity for Different Average Taskload-Driven Impact Factors
We use cutoff value to identify the intensity of impactful weather phenomena for each airport
cutoff value = 0.5 corresponds to “sometimes”, “can happen” or “several times”
cutoff value = 0.7 corresponds to “often”, “increased”, “more likely”, “higher”
cutoff value = 0.2 and cutoff value = 0.3 are close to ”rarely”, “not too much”

## Slide 11
General Numerical Thresholds for Impactful Weather Phenomena
ATCO answers (numbers can vary!)
Taszarek et al. “Hazardous weather affecting European airports: Climatological estimates of situations with limited visibility, thunderstorm, low-level wind shear and snowfall from ERA5”, Weather and Climate Extremes, vol.28, p.100243, 2020)
Taszarek et al. “A climatology of thunderstorms across Europe from a synthesis of multiple data sources”, Journal of Climate 32 (6) (2019) 1813 – 1837
European Centre for Medium-Range Weather Forecasts, ERA5: data documentation
the guidelines of the Society Automotive Engineers’ (SAE) Ground Deicing group (accepted by ICAO)
the guidelines of the World Meteorological Organization (accepted by ICAO)
Numerical Thresholds for Impactful Weather Phenomena
Convective weather (binary variable):
CAPE ≥ 1000 Jkg−1 and cp ≥ 0.075 mmh−1
Notes: Translate different intensities of the weather phenomena to the numerical values for the thresholds

## Slide 12
Airport-Dependent Numerical Thresholds for Impactful Weather Phenomena

## Slide 13
Recap: Optimization of Staff Scheduling at RTC
Input: flight movements at several RTC airports per hour
Output: Optimal assignment of controllers to RTC airports per hour
Constraints: operational + controller shift constraints (number of airports assigned to one ATCO is bounded, in multiple mode - max 2 a/p per ATCO)
B. Joseffson, T. Polishchuk, V. Polishchuk, C. Schmidt. Scheduling Air Traffic Controllers at the Remote Tower Center.
DASC 2017, St. Petersburg, USA. Awarded best in session.
Notes: E.g.: total number of moves that any ATCO handles during a period is bounded
ATCOs are assigned only to those airports, for which they hold endorsements

## Slide 14
Recap: Optimization of Staff Scheduling at RTC
Input: flight movements at several RTC airports per hour + requirements for single operation
Output: Optimal assignment of controllers to RTC airports per hour
Constraints: operational + controller shift constraints (number of airports assigned to one ATCO is bounded, in multiple mode - max 2 a/p per ATCO)
+ New constraint to force single operation
(Guarantees that airport a is operated in single mode if some impactful weather event occurs at hour h = the ATCO assigned to control airport a is not assigned any other airport at hour h)
B. Joseffson, T. Polishchuk, V. Polishchuk, C. Schmidt. Scheduling Air Traffic Controllers at the Remote Tower Center.
DASC 2017, St. Petersburg, USA. Awarded best in session.

## Slide 15
Recap: Optimization of Staff Scheduling at RTC
Input: flight movements at several RTC airports per hour + requirements for single operation
Output: Optimal assignment of controllers to RTC airports per hour
Constraints: operational + controller shift constraints (number of airports assigned to one ATCO is bounded, in multiple mode - max 2 a/p per ATCO)
+ New constraint to force single operation
(Guarantees that airport a is operated in single mode if some impactful weather event occurs at hour h = the ATCO assigned to control airport a is not assigned any other airport at hour h)
Formulated as MIP (mixed-integer program)
B. Joseffson, T. Polishchuk, V. Polishchuk, C. Schmidt. Scheduling Air Traffic Controllers at the Remote Tower Center.
DASC 2017, St. Petersburg, USA. Awarded best in session.

## Slide 16: Distribution of Necessary Number of ATCOs
We solve the MIP for each of the M EPS ensemble members and obtain the number Qm, m = 1 . . . M of ATCOs needed
The probability that at most k ATCOs are needed is:
where

## Slide 17
Experimental Study - Exemplary Historical Dates and Weather
Weather data (ECMWF): ERA5 database, Ensemble members dataset
10 ensemble members with 3-hour granularity
Choose the dates when several weather phenomena occurred at several airports:
February 16, 2020: A winter day during which four out of the five considered weather phenomena occurred: snow, low visibility, strong wind and precipitation
July 29, 2020: A summer day during which three out of the five considered weather phenomena occurred: low visibility, strong wind and precipitation

## Slide 18: Experimental Study (cont.)
Flight data (FR24): number of movements
6 cutoff values x 10 EPS members => 60 scenarios for each day
Solved MIP using AMPL Gurobi solver (60 + 60 + 2 scenarios)
Run on a powerful Tetralith server (provided by SNIC, LIU: Intel HNS2600BPB nodes with 32 CPU cores and 384 GiB RAM)

## Slide 19
Results: Distribution of the Optimal Number of Controllers
February 16, 2020 (06:00 - 14:00)
No weather impact: 5 controllers needed
With weather impact taken into account:

## Slide 20
July 29, 2020 (14:00 - 22:00)
No weather impact: 5 controllers needed
With weather impact taken into account:
Results: Distribution of the Optimal Number of Controllers

## Slide 21
Conclusions
No measures or classifications of weather impact on ATCO work exists
Proposed a method to account for weather impact on ATCO work in RTC staff scheduling
Deduced taskload-driven impact factors
Incorporated into staff scheduling framework for RTC
Presented a sensitivity analysis on the cutoff value for the taskload-driven impact factors
Used probabilistic weather products to obtain an ensemble of staffing solutions
Obtained example probability distributions for optimal number of controllers
Demonstrated that ignoring weather impact can lead to understaffing

## Slide 22: References
A. Lemetti, T. Polishchuk, R. Sáez, X. Prats. Evaluation of Flight Efficiency for Stockholm Arlanda Airport Arrivals. In DASC 2019, San Diego.
A. Lemetti, T. Polishchuk, R. Sáez. Evaluation of Flight Efficiency for Stockholm Arlanda Airport using OpenSky Network Data. In OpenSky Workshop 2019, Zürich.
A. Lemetti, T. Polishchuk, R. Sáez, X. Prats. Analysis of Weather Impact on Flight Efficiency for Stockholm Arlanda Airport Arrivals. In EIWAC 2019, Tokyo.
A. Lemetti, T. Polishchuk, V.Polishchuk, R. Sáez, X.Prats. Identification of Significant Impact Factors on Arrival Flight Efficiency within TMA. In ICRAT 2020.
V. Bulusu, H. Hardell, A. Lemetti, T. Polishchuk, V. Polishchuk, E. Royo. Morphing STARs vs drones and weather in TMA. In ICRAT 2020.

## Slide 23: References (cont.)
H. Hardell , A. Lemetti, T. Polishchuk. Arrival Flight Efficiency in Numbers: What New the Covid-19 Crisis is Bringing to the Picture? In SIDs 2020.
B. Josefsson, A. Lemetti, T. Polishchuk, V. Polishchuk, C. Schmidt. Integrating Weather Impact in RTC Staff Scheduling. In SIDs 2020.
On-going work
E. Hernandez-Romero, B. Josefsson, A. Lemetti, T. Polishchuk, C. Schmidt. Integrating Weather Impact in Air Traffic Controller Shift Scheduling in Remote and Conventional Towers. Submitted to EURO Journal on Transportation and Logistics (accepted for publication after revision).
H. Hardell, A. Lemetti, T. Polishchuk. Evaluation of COVID-19 Impact on Arrival Flight Efficiency at Stockholm Arlanda and Göteborg Landvetter Airports (Journal paper)

## Slide 24
THANK YOU!
e-mail: Anastasia.Lemetti@liu.se